Competitive Enzyme Immunoassay Kit for

Quantitative Analysis of Gentamicin

1. Background

Gentamicin is an aminoglycoside antibiotic, which is broadly applied in animal disease treatment. For it has neurotoxicity and kidney toxicity, its residue in animal-derived food is harmful to human, it is strictly controlled in use in EU,US and China. At present, ELISA is the common approach in supervision and control of this drug.

This kit is a new product for drug residual detection based on ELISA technology, which only costs 1.5h in each operation and can considerably minimize operation errors and work intensity.

2. Test Principle

This kit is based on indirect-competitive ELISA technology. The microtiter wells are coated with coupling antigen. Gentamicin residue in the sample competes with the antigen coated on the microtiter plate for the antibody. After the addition of enzyme labeled anti-antibody, TMB substrate is used to show the color. Absorbance of the sample is negatively related to the Gentamicin reside in it, after comparing with the Standard Curve, multiplied by the dilution multiple, Gentamicin residue quantity in the sample can be calculated.

3. Applications

This kit can be used in quantitative and qualitative analysis of Gentamicin residue in animal tissues (muscle and liver ,etc.)

4. Cross-reactions

Gentamicin……………………………………100%

streptomycin…………………………………………<1%

dihydrostreptomycin …………………………………<1%

Neomycin ………………………………………………<1%

5. Materials Required

5.1 Equipments

┅┅Microtiter plate spectrophotometer (450nm/630nm)

┅┅Rotary evaporator or nitrogen drying instruments

┅┅Homogenizer (or stomacher)

┅┅shaker

┅┅gyroscope  or vortex mixer

┅┅centrifuge

┅┅Analytical balance (inductance: 0.01g)

┅┅Graduated pipette: 10ml

┅┅Rubber pipette bulb

┅┅volumetric flask：1L

┅┅polystyrene centrifuge tube：2ml、50ml

┅┅Micropipettes: 20(l～200(l、200(l～1000(l

250(l-multipipette

5.2 Reagents

---- disodium hydrogen phosphate dodecahydrate  (AR)

----Sodium chloride (AR)

---- Sodium hydroxide (AR)

----potassium dihydrogen phosphate dihydrate (AR)

----potassium chloride (AR)

----deionized water

6. Kit Components

1. Microtiter plate with 96 wells coated with coupling antigen

2. Standard solutions(6 bottles×1ml/bottle)

0ppb，0.1ppb，0.3ppb，0.9ppb，2.7ppb，8.1ppb

3. High concentration standard control: (1ml/bottle) 1ppm

4. Enzyme-labeled secondary antibody 12ml ………red cap

5. Antibody solution 7ml …………………………… green cap

6. Solution A 7ml…………………………………...…white cap

7. Solution B    7ml…………………………………..red cap

8. Stop solution  7ml………………………….……yellow cap

9. 20×concentrated wash solution 40ml…… transparent cap

10. 2×concentrated extraction solution 50ml………blue cap

7. Reagents Preparation

Solution 1: 0.1M PBS buffer solution (PH=10-11)

Weigh 13.4g disodium hydrogen phosphate dodecahydrate, .20g sodium chloride, 0.32g Sodium hydroxide , 0.5g potassium dihydrogen phosphate dehydrate and 0.5g potassium chloride, dissolve with deionized water to 500ml;

Solution 2: Wash solution

Dilute the 20×concentrated wash solution with deionized water in the volume ratio of 1:19, which will be used for washing the plates. This solution can be stored at 4℃ for 1 month.

Solution 3: Extraction solution

Dilute the 2×concentrated extraction solution with deionized water in the volume ratio of 1:1, which will be used for sample extraction, This solution can be stored at 4℃ for 1 month.

8. Sample Preparations

8.1 Notice and precautions for the users before operation

a. Please use one-off tips in the process of experiment, and change the tips when absorb different reagent.

b.Make sure that all experimental instruments are clean ,otherwise it will effect the assay result.

c. Keep untreated samples in freeze ;

d. Treated samples can not be conserved for over 12h, which must be tested in time;

8.2 Chicken , chicken liver

---- Weigh 2.0±0.05g comminuted degreased tissue sample into a 50ml polystyrene centrifuge tube, then add 6ml 0.1M PBS (PH=10~11) buffer solution(See solution 1), mix completely;

----Incubate for 60min in 60℃ water bath, take out and cool to room temperature and mix completely;

----Centrifuge at room temperature for 10min, at least 3000g ;

----Transfer the supernate, then dilute with extraction solution(see solution 3) in the volume ratio of  1:9, (50(l supernate + 450 (l extraction solution);

----Take 50(l of the prepared solution for assay;

9. Assay process

9.1 Notice before assay

9.1.1 Make sure all reagents and microwells are all at room temperature (20-25℃).

9.1.2 Return all the rest reagents to 2～8℃ immediately after used.

9.1.3 Washing the microwells correctly is an important step in the process of assay; it is the vital factor to the reproducibility of the ELISA analysis.

9.1.4 Avoid the light and cover the microwells during incubation.

9.2 Assay Steps

9.2.1 Take all reagents out at room temperature (20-25℃) for more than 30min, homogenize before use.

9.2.2 Get the microwells needed out and return the rest into the zip-lock bag at 2-8℃ immediately.

9.2.3 The diluted wash solution should be rewarmed before use;

9.2.4 Number: Number every microwell position and all standards and samples should be run in duplicate. Record the standards and samples positions.

9.2.5 Add standard solution/sample: Add 50µl of standard solution or prepared sample to corresponding wells. Add 50µl antibody solution. Mix gently by shaking the plate manually and incubate for 30min at 37℃ with cover.

9.2.6 Wash: Remove the cover gently and pure the liquid out of the wells and rinse the microwells with 250µl diluted wash solution (see solution 2) at interval of 10s for 4~5 times. Absorb the residual water with absorbent paper (the rest air bubble can be eliminated with unused tip).

9.2.7 Add enzyme labeled secondary antibody solution: Add 100µl of enzyme labeled secondary antibody solution to each well, Mix gently by shaking the plate manually and incubate for 30min at 37℃ with cover, take out and repeat the wash step;

9.2.8 Coloration: Add 50µl solution A and 50µl solution B to each well. Mix gently by shaking the plate manually and incubate for 15 min at 37℃ with cover (see 12.8).

9.2.9 Measure: Add 50µl the stop solution to each well. Mix gently by shaking the plate manually and measure the absorbance at 450nm against an air blank (It’s suggested measure with the dual-wavelength of 450/630nm. Read the result within 5min after addition of stop solution. ) (We can also measure by sight without stop solution in short of the ELIASA instrument).

10. Results

There are 2 different methods to determinate the results. Method 1 leads to a round estimation, and method 2 leads to definite quantity estimation. (Please notice: the absorption is inversely proportional to the Gentamicin concentration in the sample.)

10.1 Round estimation

We can get the range of different strengths from the compare of average absorption and standards by sight. For example, the absorption of sample 1 is 0.512, sample 2 is 0.899, and the absorptions of Gentamicin standard solutions: 1.900(0ppb); 1.450(0.1ppb); 1.000(0.3ppb); 0.600(0.9ppb); 0.300(2.7ppb); 0.150(8.1ppb). So we can say the strength of diluted sample 1 is between 0.9ppb and 2.7ppb; and diluted sample 2 between 0.3ppb to 0.9 ppb. In order to obtain the Gentamicin actually contained in a sample, the diluted sample results must be further multiplied by the corresponding dilution multiple.

10.2 Definite quantity estimation

(1) The mean values of the absorbance values obtained for the standards and the samples are divided by the absorbance value of the first standard (zero standard ) and multiplied by 100%. The zero standard is thus made equal to 100% and the absorbance values are quoted in percentages.

B

Absorbance (%) = —— ×100%

B0

B ——absorbance standard (or sample)

B0 ——absorbance zero standard

(2) To draw a standard curve: Take the absorbance value of standards as y-axis, semi logarithmic of the concentration of the Gentamicin standards solution (ppb) as x-axis.

--- The Gentamicin concentration of each sample (ppb), which can be read from the calibration curve, is multiplied by the corresponding dilution multiple of each sample followed, and the actual concentration of sample is obtained.

For evaluation of the ELISA kits special software has been developed for exact and rapid analysis. The analysis software can be ordered on request.

Dilution multiple of samples:

Muscle and liver samples : 40

11. Sensitivity, accuracy and precision

Test Sensitivity：0.1ppb

Detection limit：

Chicken, chicken liver……………………………………… 4pp

Accuracy:

Chicken, chicken liver………………………………… 90±10%

Precision:

Variation coefficient of the ELISA kit is less than 10%.

12. Notice

12.1 The mean values of the absorbance values obtained for the standards and the samples will be reduced if the reagents and samples have not been regulated to room temperature (20-25℃).

12.2 Do not allow microwells to dry between steps to avoid unsuccessful reproducibility and operate the next step immediately after tap the microwells holder.

12.3. Homogenize each reagent before using.

12.4. Keep your skin away from the stop solution for it is the 2M H2SO4 solution.

12.5 Don’t use the kits out of date. Don’t exchange the reagents of different batches, for it will drop the sensitivity.

12.6 Storage condition:

Keep the ELISA kits at 2-8℃,do not freeze. Seal rest microwell plates Avoid straight sunlight for the standard sample and the colorless chromogenic reagent are sensitive to light.

12.7 Indications for the reagents going bad:

Substrate solution should be abandoned if it turns colors.

The reagents may be turn bad if the absorbance value (450/630nm) of the zero standard is less than 0.5(A450nm＜0.5).

12.8 The coloration reaction needs 10-15 min after adding Solution A and Solution B. And you can prolong the incubation time if the color is too light to be determined. never exceed 30min,On the contrary, shorten the incubation time properly.

12.9 The optimal reaction temperature is 37℃. Higher or lower temperature will lead to the changes of sensitivity and absorbance values.

13. Storage condition and storage period

Storage condition: 2-8℃.

Storage period: 6 months.