Favor Fast Centrifuge

This benchtop centrifuge for all teaching laboratory applications is CE approved. This sturdy 12-place centrifuge is supplied with a rotor that accommodates either 1.5 or 2.0 ml tubes. The motor is brushless and requires no routine maintenance. Quick-spin features, Max RPM 14,500 /Max Force 14,000g, the motor is brushless and requires no routine maintenance.

Features

- Fashion design and succinct outlook.

- Safe for cold room operation.

- Microprocessor controller with digital performance

- Fast acceleration and deceleration.

- LCD monitor.

- User Calibration.

- Quick-spin features.

- Max RPM 14,500 /Max Force 14,000g.

- Rotor could be sterilized.

- The motor is brushless and requires no routine maintenance.

- CE certification

Specification

| Controller | Digital Microprocessor controller |
| --- | --- |
| Display | LCD |
| Operating Temperature | 5~35℃ |
| Max RPM Max Force | 14,500rpm 14,000×g |
| Max Capacity | 12 × 1.5/2.0ml tubes |
| Timer | 15 seconds ~99 minutes |
| Time to Max speed | 25 seconds |
| Time deceleration from Max speed | 18 seconds |
| Ability to set by RPM, RCF, and toggle between display modes | Yes |
| Rated Voltages | 110V/220V selectable |
| Unit Dimension | W240 x L212 x H138 mm |
| Weight (includes rotor) | 4.5 kg |

Ordering Information

| Catalog # | Product Name | Max Capacity | Max Temp | Dimensions (LxWxH) |
| --- | --- | --- | --- | --- |
| FACTF 001 | Favor Fast Centrifuge | 12 × 1.5/2.0ml tubes | 5℃ ～ 35℃ | 212mm×240mm×138mm |