Favorgen Galaxy 230 Colony Counter

Description

Favorgen Galaxy 230 Colony Counter is specially designed for reliable and traceable counting of bacterial colonies growing on nutrient agar in Petri dishes with a wide range of diameter from 60mm and 90-150mm.  Innovation PC software empower you recording, tracing or reporting data of sample number, date, user’s name, row count, dilution factor, total count and so on very easily..  Pressure sensor design enables the counter being operated by any marking pen.  The glare-free light without blinding or noise, which comes from ring-shaped illumination lamp with electronic ballast, make operator working comfortable without eyestrain.  Unique BACK button allow users to deduct data whenever over counting.  Contrast-plate with white and black side is supplied for using dark or clear agar.

Features

- Wide range size of Petri dish holder for easy use.

- Pressure sensor design for any marking pen

- Background plate changeable (white or black) for using dark or clear agar.

- Unique BACK button design for deducting data when over counting.

- No-glare illumination for working comfortable without eyestrain..

- Adjustable pressure sensitivity and acoustical counting signal.

- Innovation PC software for tracing, reporting or recording data of sample No., date, user’s name, row count, dilution factor, total count etc. reliably and easily.

Specification

| Readout: | 4-Digit (0-9999) bright red0.6” LED display |
| --- | --- |
| Magnification: | 2-3x |
| Petri dish size: | 60mm and 90-150mm diameter |
| Zero reset: | yes |
| Count back: | yes |
| Illumination: | Glare-free ring-shaped lamp |
| Pressure sensitivity: | adjustable |
| Acoustical counting signal: | adjustable |
| Out put: | RS232 and USB2.0 |
| Dimension: | W313mm x H360mm x D346mm |
| Weight: | Net: 5.2KG Shipping: 6.4KG |

Ordering Information

| Catalogue No. | Contents |
| --- | --- |
| FACLC 175200-11 | 1. Galaxy 230 colony counter 2. Power AC 110V, 60Hz 3. Marking pen (black) x1 |
| FACLC 175200-22 | 1. Galaxy 230 colony counter 2. Power AC 220V, 60Hz 3. Marking pen (black) x1 |
| FACLC 175300-11 | 1. Galaxy 230 colony counter 2. Power AC 110V, 60Hz 3. Marking pen (black) x1 4. PC Software |
| FACLC 175300-22 | 1. Galaxy 230 colony counter 2. Power AC 220V, 60Hz 3. Marking pen (black) x1 4. PC Software |
| FACLC 175200-48 | STAEDTLER 4 color (black, red, blue, green) marking pen set 0.4mm/permanent ink |
| FACLC 175300-12 | PC software w/ connecting cable for Galaxy 230 colony counter |